## Slide 1: RESET
Reset circuit:
Two types:
Active high reset circuit (RST/RESET)
Active low reset circuit (RST/RESET)

## Slide 2: Power on reset circuit
In order to reset the controller, minimum two machine cycles time is required.
If 12MHZ crystal oscillator is connected, 1MC will take 1 micro second
i.e. minimum 2 microseconds time is required to reset the controller.

## Slide 3: Power on reset circuit with switch for run time reset

## Slide 4: CRYSTAL CKT
C1, C2 = 30 pF ± 10 pF for Crystals (in between 20pF to 40pF)
= 40 pF ± 10 pF for Ceramic Resonators (in between 30pF to 50pF)

## Slide 5
www.vectorindia.org
8051 Block Diagram
Interrupt
Control
External Interrupts
CPU
OSC
Timer 1
Timer 0
Serial
Port
I/O Ports
Bus
Control
Counter
Inputs
P0
P3
P1
4k byte
ROM
128 byte
RAM
P2
(Address / Data)
TXD
RXD
1MHz-16MHz

## Slide 6
Minimum hardware requirements for 8051 CPU:
Power supply
Pullup for PORT0
Reset circuit
Crystal circuit
EA(bar)/VPP pin is connected to VCC (in order to access the on-chip ROM)
ISP connections (used for hex file loading to the flash memory)