## Slide 1: Instruction Set & Programming
What are Addressing Modes ?
How many Addressing Modes does 8051 support ?
And what are they ?
What is Assembly language ?
What is 20/80% rule of assembly language programming ?
Snytax of Assembly language.
Explanation of Addressing Modes

## Slide 2: 5 Addressing Modes
Immediate Addressing Mode
Register Addressing Mode
Direct Addressing Mode
Indirect Addressing Mode
Indexed Addressing Mode

## Slide 3
What is Assembly language ?
A low level machine specific abstracted programming language which uses symbolic representations for opcodes & operands for instructions machine codes .
Syntax of Assembly
LABEL: MNEMONIC OPERANDS ; COMMENTS

## Slide 4: Categories/groups of Instructions
Data Transfer
Arithematic
Logical
Boolean
Branching

## Slide 5: Understanding Addressing Modes using MOV instruction
Syntax:
MOV Destination,Source

## Slide 6: Immediate addressing
  The value of a constant can follow the opcode in program memory
  The # sign is the designator of the constant

## Slide 7
Options:
MOV A,#data(8-bit)
MOV Rn,#data(8-bit) ; n=0 - 7
MOV DPTR,#data (16-bit)
MOV @Ri,#data(8-bit) ; i=0/1

## Slide 8: Register Addressing mode
options :
MOV A,Rn ; n=0 - 7
MOV Rn, A ; n=0 -7

## Slide 9
Direct Addressing
  At least one of the operand is specified by an 8 bit address field
  Internal data RAM and SFRs can be directly addressed

## Slide 10: Direct Addressing
Options :
MOV Addr,#data(8-bit)
MOV A,Addr
MOV Addr,A
MOV Rn,Addr
MOV Addr,Rn
MOV Addr1,Addr2

## Slide 11: Indirect Addressing
  The instruction specifies a register that contains the address of the operand
  Both Internal and External RAM can be indirectly addressed
  Address register can be R0 or R1 of a selected register bank or the SP for 8 bit and DPTR for 16 bit address

## Slide 12: Indirect : Internal RAM
options:
MOV @Ri,A ; i=0/1
MOV A,@Ri ; i = 0/1
MOV @Ri,ADDR
MOV ADDR,@Ri

## Slide 13: Indirect: External RAM
Notes:
All external data moves must involve A register
Rp,where p=0/1 can address 256 bytes;
DPTR can address 64K bytes
MOVX is normally used with external RAM or I/O address.

## Slide 14: Indirect : External
Options:
MOVX @Rp,A ;p=0/1
MOVX A,@Rp ; ”
MOVX @DPTR,A
MOVX A,@DPTR

## Slide 15: Indexed Addressing ONLY for: Code Memory Read
Options:
MOVC A,@A + DPTR
MOVC A,@A + PC

## Slide 20: END of ADDRESSING MODES Discussion

## Slide 22: Data Transfer Instruction Set
Continued

## Slide 23: Push and Pop opcodes
PUSH Addr
POP Addr

## Slide 26: Notes
When SP reaches FFh, it rolls over to 00h
PUSHes above 7Fh result in error
Only direct addresses MUST be used as operands
But PUSH & POP use indirect addressing

## Slide 27: Data Exchanges
Move data in two directions
XCH A, Rn
XCH A, addr
XCH A,@Ri
XCHD A, @Ri

## Slide 28: Notes
All exchanges are internal to 8051
All exchanges use register A
When using XCHD, the upper nibbles are not exchanged