## Slide 1: CAN PROTOCOL IMPLEMENTATION (LOW LEVEL CAN DRIVER/FIRMWARE) USING LPC2129 uC & Keil Embedded C for ARM LEVEL 2

## Slide 2: CAN Controller SFRs in LPC2129 uC Additionally May Be Required
CAN 1 Controller SFRs
C1ICR
C1IER
C1EWL
CAN 2 Controller SFRs
C2ICR
C2IER
C2EWL
SFF_sa
SFF_GRP_sa
EFF_sa
EFF_GRP_sa
ENDofTable

## Slide 3: CAN Initialisation For Message Filteration
For CAN Communication- Reception

## Slide 4
/* CAN Controller 1 Initialization : (defined in can.c ) */
//declare pointer for Acceptance Filter RAM Base Address in LPC2129
u32 *stdFilter=(u32 *)ACC_FILTER_RAM_BASE_ADDR;
  void Init_CAN1(void)
  {
  //cfg p0.25 pin as CAN1_RX pin(RD1),TD1 is exclusive using PINSEL1
  //Reset CAN1 controller using C1MOD
  //Set baud Rate for CAN using C1BTR
  //Disable Acceptance Filter using AFMR =1
  //Now Configure IDs to accepted in Filter Table/Ram
stdFilter[0]=0x20012002;//allow ids 1 & 2
stdFilter[1]=0x20032004;//allow ids 3 & 4

## Slide 5
/* CAN Controller 1 Initialization Cont’d: (defined in can.c ) */
tdFilter[2]=0x20072008;//allow ids 7 & 8
stdFilter[3]=0x2009200A;//allow ids 9 & A
//set start address of std table SFF_sa=0x00000000
  //set start addr of std group table SFF_GRP_sa=16;
  //set start addr of ext table EFF_sa=16
  //set start addr of ext group table EFF_GRP_sa=16;
  //set end of table address ENDofTable=16;
  //enable acceptance filters AFMR=0;
  //Enable CAN1 controller C1MOD=0;
  }

## Slide 6: Now Using Keil IDE To
Simulate CAN Communication-Reception